## Slide 1: Network Observability Measurements

## Slide 2: Testbed Setup - Ingress
receiver
Pktgen
Observ Agent
Tcnode7
Kernel 5.13
Tcnode6
Kernel 5.4
Questions?
How much % of traffic is successfully monitored by “Observ agent”
What are the overheads?
Observ Logs/Metrics
Eth_protocol, Src_Mac, Dst_Mac, Src_IP, Dest_IP, Src_Port, Dst_port, Protocol =>
Packets, Bytes, FlowStartTime, FlowEndTime
100M
3.7 Mpps (64B packets)
40 Flows:
1 Flow/Thread
40 Gbps

## Slide 3: Results – Monitoring Ingress
Agent | Packets Sent | Packets Monitored | Monitoring efficacy(%) | Process CPU(%) 1 Core | Overall CPU(%) 80 cores | Mem (KB)
pmacct(print) | 101,898,951 | 52,978,667 | 51.99 | 185 | 16.1 | 89,268
tcpdump | 101,834,300 | 68,618,717 | 67.38 | 45 | 24 | 27,400
netobserv-ebpf-agent_v1 | 102,109,078 | 9,223,414 | 9 | 195 | 10.07 | 1,706,628
netobserv-ebpf-agent_v2 | 100,279,611 | 100,279,611 | 100 | 0.2 | 3.7 | 1,780,468
None | 101,228,092 | 0 | 0 | - | 3.11 | -
Packet Rate (Mpps) = ~3.7 Mpps

## Slide 4: Testbed Setup - Egress
pktgen
receiver
Observ Agent
Tcnode7
Kernel 5.13
Tcnode6
Kernel 5.4
Questions?
How much does “Observ agent” slow down “pktgen”
How much % of traffic is successfully monitored by “Observ agent” (monitoring rate)
Observ Logs/Metrics
Eth_protocol, Src_Mac, Dst_Mac, Src_IP, Dest_IP, Src_Port, Dst_port, Protocol =>
Packets, Bytes, FlowStartTime, FlowEndTime
100M (64B packets)
4.7 Mpps
40 Flows:
1 Flow/Thread
40 Gbps

## Slide 5: Results – Monitoring Egress
Agent | Packets Sent | Packets Monitored | Packet Rate (Mpps) | Monitoring efficacy(%) | Process CPU(%) 1 Core | Overall CPU(%) 80 cores | Mem (KB)
pmacct(print) | 101,636,497 | 65,574,533 | 2.32 | 64.5 | 186 | 51.79 | 89,268
tcpdump | 100,374,690 | 100374690 | 1.65 | 100 | 51 | 51.5 | 27,400
netobserv-ebpf-agent_v1 | 101,186,109 | 13,037,588 | 2.6 | 12 | 170 | 55.2 | 1,706,628
netobserv-ebpf-agent_v2 | 101,300,570 | 101300570 | 4.45 | 100 | 0.2 | 48.54 | 1,780,468
Native | 101,537,206 | 0 | 4.7 | - | - | 48.5 | -
5 Runs : On each run, 100Million packets are sent out through the interface
Chart: 
| pmacct | tcpdump | netobserv-ebpf-agent_v1 | netobserv-ebpf-agent_v2 | None
Throughput (Mpps) | 2.32 | 1.65 | 2.6 | 4.45 | 4.7

## Slide 6: Pmacctd Config
daemonize: true
pcap_interface: ens6f0np0
plugins: print[flows]
!
aggregate[flows]: src_mac, dst_mac, src_host, dst_host, src_port, dst_port, proto
!
print_output_file[flows]: /home/pravein/pmacctd/flows-%Y%m%d_%H%M.txt
print_output[flows]: csv
print_refresh_time[flows]: 100
print_history[flows]: 5m
print_output_file_append[flows]: true
!
print_latest_file[flows]: /home/pravein/pmacctd/flows-latest